## Slide 1
0. Doff PAPR + Gown
1. Prepare to Doff
2. Engage trained observer
3. Disinfect outer gloves
4. Remove outer apron
5. Disinfect outer gloves
6. Remove outer boots
7. Disinfect outer gloves
No
Yes
Plan 4: Is apron used?
8. Remove outer gloves
9. Inspect inner gloves
10. Remove PAPR
11. Remove hood
12. Remove gown
13. Disinfect inner gloves
14. Disinfect shoes
15. Disinfect inner gloves
16. Remove inner gloves
17. Perform hand hygiene
18. Inspect body for contamination
19.Exit doffing area
Plan 0: do 1 through 19 in order in accordance with trained observer instructions

## Slide 2
1. [HCW] Prepare to doff
Plan 1.1 Visible Contamination?
1.1 [HCW] Inspect PPE
1.1.1 [HCW] Disinfect surface of PPE with EPA-registered disinfectant
1.2 [HCW] Disinfect outer gloves
1.2.1 Follow procedure for step 3.2-3.4
1.3 [HCW] Signal TO
1.3.1 [HCW] Wait for 1.4
1.4 [TO] Signal doffing area is clear
1.5 [HCW] Enter doffing area
No
Yes
Plan 1: do 1.1 to 1.5 in order

## Slide 3
2. [HCW]Engage TO
2.1 [TO] Review goals & hazards
2.2 [TO] Instruct HCW to examine PPE
Plan 2.2 Rip, tear, or contamination?
Rip/tear – Follow breach protocol
Contamination: Disinfect surface of PPE with EPA-registered disinfectant
No
Yes
Plan 2: do 2.1 to 2.2 in order
exit

## Slide 4
3. [HCW] Disinfect outer gloves
3.1 [HCW] Examine for contamination
Plan 3.1 Visible Contamination?
Yes
3.1.1 [HCW] Apply EPA-registered wipe to contaminated area
No
3.2 [HCW] Apply ABHR to palm or EPA-registered disinfectant wipe
3.3 [HCW] Rub top/bottom of both hands and in between fingers and thumbs
3.4 [HCW] Wait for gloves to dry
Plan 3 : do 3.1 to 3.4 in order

## Slide 5
4. Remove outer apron
4.1 [TO/Asst.] Untie strap
4.2 [HCW] Remove apron
Can apron be pulled away at neck?
Yes
4.2.1 [HCW] Tear apron at neck
No
4.2.3 [HCW] Pull apron away from body
4.3
4.2.2 [HCW] Lift strap over head
4.3 [HCW] Roll apron inside to outside
4.4 [HCW] Discard apron into waste receptacle
4.5 [HCW] Inspect PPE
Plan 4.5. Rip, tear, or contamination?
No
Yes
exit
5. Disinfect outer gloves
Plan 5: do step 3 in order
Plan 4: do 4.1 to 4.5 in order
4.5.1
Rip/tear – Follow breach protocol
Contamination: Disinfect surface of PPE with EPA-registered disinfectant

## Slide 6
6. [HCW] Remove boot covers
6.1 [HCW]Sit in chair designated for shoe/boot removal
6.2 [HCW] Take off first boot cover
6.2.1 [HCW/Asst] Grasp outside of bootie
6.2.2 [HCW] Pull down toward ankle
6.2.3 [HCW]] Lift bootie over heal
6.2.4 [HCW]] Pull bootie off foot
6.3 [HCW] Dispose of bootie in waste receptacle
6.4 [HCW] Take off second boot cover (see 6.2 to 6.3)
7. Disinfect outer gloves
Plan 7: do step 3 in order; If Asst. helped, do step 3 in order
Plan 6: do 6.1 to 6.4 in order
Plan 6.2: do 6.2.1 to 6.2.4 in order then exit

## Slide 7
8. [HCW] Remove outer gloves
8.1.1 [HCW] Hold wrist with thumb pointed at ceiling
8.1 [HCW] Take off first glove slowly
8.1.2 [HCW] Pinch glove and lift at wrist
8.1.3 [HCW] Roll glove down until it is off the hand in a ball
8.1.4 [HCW] Hold balled glove in palm of other gloved hand
8.2 [HCW] Remove second glove slowly
8.2.1 [HCW] Slide a finger down &inside the outer glove
8.2.2 [HCW] Pull off second glove until balled around first glove
8.3 [HCW] Dispose of gloves in waste receptacle
Plan 8: do 8.1 to 8.3 in order
Plan 8.1: do 8.1.1 to 8.1.4 in order then exit
Plan 8.2: do 8.2.1 to 8.2.2 in order then exit

## Slide 8
9. [HCW] Inspect both inner gloves
9.1 [HCW] Inspect palms, backs of hands, and fingers
Plan 9.1 Rip, tear, or contamination?
No
Yes
9.1.2 Remove inner glove (follow step 16)
9.1.3 Discard inner gloves into waste receptacle
9.1.4 Perform hand hygiene with ABHR
(see 17)
9.1.5 Put on new set of gloves up to the edge of gown sleeve
9.2 [HCW] Disinfect inner gloves (see 13)
Plan 9: do 9.1 to 9.2 in order
Plan 9.1.1: do 9.1.1 to 9.1.5 in order then exit
9.1.1
Rip/tear – Follow breach protocol
Contamination: Disinfect surface of PPE with EPA-registered disinfectant

## Slide 9
10. Remove PAPR
10.1 [Asst.] Detach hose at the hood
10.2 [Asst.] Turn off system
10.3 Unclip belt
10.3.1 [Asst.] Hold belt unit in hands
10.3.2 [HCW] Unclip belt
10.4 [Asst.] Place reusable PAPR components in designated area
10.5 [HCW/Asst.] Disinfect gloves (13)
Plan 10: do 10.1 to 10.5 in order according to manufacturer instructions
Plan 10.3.1: do 10.3.1 to 10.3.2 in order then exit

## Slide 10
11. Remove hood
11.1 [Asst.] Grab outside of HCWs hood
11.2 [Asst.] Roll hood up towards top of shoulders
11.3 [Asst.] Form cuff with hood
11.4 [TO] Signal for HCW to slowly remove hood
11.5 [HCW] Grab hood near ears
11.6 [HCW] Bend forward at waist
11.7 [HCW] Pull hood slowly down and away from head until at waist level
11.8 [HCW] Discard hood in waste receptacle
11.9 [HCW/Asst] Disinfect gloves (see 13)
Plan 11: do 11.1 to 11.9 in order then exit

## Slide 11
12. Remove gown
12.1 [HCW] Release tie
12.2 [HCW] Pull gown slowly away from body until off shoulders
12.3 [HCW] Pull gown all the way down off one arm
12.4 [HCW] Pull gown down all the way down off other arm
12.5 [HCW] Roll gown inward , away from body, until it is in a tight ball
12.6 [HCW]]Dispose of gown in waste receptacle
13. Disinfect inner gloves
Plan 12: do 12.1 to 12.6 in order
13.1 [HCW] Apply ABHR to palm or EPA-registered disinfectant wipe
13.2 [HCW] Rub top/bottom of both hands and in between fingers and thumbs
13.3 [HCW] Wait for gloves to dry
Plan 13 : do 13.1 to 13.3 in order

## Slide 12
14. Disinfect shoes
14.1 Sit in clean chair
14.2 Get EPA-registered disinfectant wipes
14.3 Apply disinfectant wipe to first shoe
14.3.1 Move wipe from top to bottom across all surface area
14.4 Apply disinfectant wipe to second shoe (see 14.3.1)
15. Disinfect inner gloves
(see 13)
Plan 14: do 14.1 to 14.4 in order
16. Remove inner gloves
Plan 16 : do 8.1 to 8.3 in order

## Slide 13
17. Perform hand hygiene
18. Inspect body for contamination
18.1 [HCW]Hold out both arms to side
18.2 [HCW] Slowly turn around
18.3 [HCW/TO/Asst] Inspect for rips, tears, or contamination
Plan 18.3 Rip, tear, or contamination?
Proceed to the breach protocol
No
Yes
exit
19. Exit doffing area
Plan 18: 18.1 to 18.3 in order
17.1 [HCW] Apply ABHR to palm
17.2 [HCW] Rub top/bottom of both hands and in between fingers and thumbs
17.3 [HCW] Wait for hands to dry